First stage: Parsing

The input string from the user is transformed into a parse-form representing a composite (see terminology.odt).

Examples:
“dua” →	dua
“dua pai” →	(dua pai)
“dua leo pai” →	(dua (leo pai))
“dua leo ru pai” →	(dua (ru leo pai))

This stage must support:
1. predicate predicate
2. predicate RU predicate
3. TO RU predicate TO predicate
4. MU predicate

There are four types of parse-forms:
1. P	where P is a predicate word
2. (X Y)	where X and Y are parse-forms
3. (mu X)	where X is a parse-form
4. (ru X Y)	where X and Y are parse-forms and ru is a member of RU

(parse exp) =
1. anything TO RU p1 TO p2	→ (parse anything (RU (parse p1) (parse p2)))
2. anything1 MU p1 anything2	→ (parse anything1 (MU p1) anything2)
3. anything p1 RU p2 p3...	→ (parse anything (RU p1 p2) p3...)
4. p1	→ p1
5. p1 p2...	→ (p1 (parse p2...))

...where all p are parse-forms

Second stage (hidden): Interpretation and Expansion

First, the parse-form is used to generate a list of serial-forms, cycling through the combinations of predicates that go with the words. Some combinations may be filtered out.

Then, the serial-forms are expanded via (expand), (mu-ify), and (ru-ify).

These two steps are placed in the same stage because eventually, filtration modes may be necessary which can only be done “in line” with the expansion. For example, there may be a mode where if the head of the serial has type [x 1 x], then the tail must be filtered out to only its highest-arity predicate.

Third stage: Pretty-print

Both the serial-forms and the resulting expanded predicates can be pretty-printed.